## Slide 1: Watershed-based Solutions to Increase Resilience to Harmful Algal Blooms in Santuit Pond in a Warmer and Wetter Climate
MVP Action Grant
Core Team Project Initiation Meeting
September 28, 2021

## Slide 2: Agenda
Welcome
MVP Action Grant
Project Purpose
Core Team & Contacts
Background – Cyanobacteria, Climate Change, Watershed Practices
Tasks & Timeline
Opportunities for Input
Outcomes
Questions/Discussion

## Slide 3: MVP Action Grant
Municipal Vulnerability Preparedness (MVP) Program
Planning for climate change resiliency
Implementing priority projects
Mashpee MVP Planning Grant – March 2020
  https://www.mass.gov/doc/mashpee-report/download
Top Priorities
  Coastal Green Infrastructure
  Water Quality
  Stormwater Infrastructure
  Vulnerability for Municipal Facilities & Infrastructure
  Emergency Management Planning & Communication
  Low-lying Roadways & Culverts

## Slide 4: Project Purpose
Santuit Pond – chronic cyanobacteria blooms
Changing climate favors cyanobacteria
Nutrients (internal and external) drive blooms
Focus on watershed (external) to reduce nutrient inputs
  Green Stormwater Infrastructure
  Residential Low Impact Development (LID) Practices

## Slide 5: Project Team Primary Contacts
Town of Mashpee
  Ashley Fisher, Director of Natural Resources, afisher@mashpeema.gov, 508-539-1410
Mashpee Wampanoag Tribe
  Jason Steiding, Natural Resources Dept. Director, Jason.Steiding@mwtribe-nsn.gov
Mashpee TV
  Christopher Ball, chris@mashpeetv.com
Fuss & O’Neill
  Diane Mas, Project Manager, dmas@fando.com, 800-286-2469 x4406

## Slide 6: Cyanobacteria
Cyanobacteria
  Bacteria (not a true algae) that photosynthesize
  Produce toxins harmful to people and animals
    Harmful Algal Bloom (HAB or CyanoHAB)
  Deplete oxygen in water
  Aesthetics (sight & smell)

## Slide 7: Cyanobacteria & Changing Climate
Nutrients (phosphorus) + warm water + still water = CyanoHABs
Summer temperatures >> total phytoplankton
Length of summer >> cyanobacteria abundance
New England is anticipated to experience an increase in number of days with blooms sooner than other areas of the U.S.
Average summer temperatures 3-5 degrees by mid-century, 5-9 degrees higher by the end of the century
Growing degree days 26% under moderate emissions by mid-century
Sources: Chapra et al. (2017); Ho and Michalack (2019); Northeast Climate Science Center at the University of Massachusetts Amherst (https://www.resilientma.org/)

## Slide 8: Cyanobacteria & Changing Climate
Nutrients (phosphorus) + warm water + still water = CyanoHABs
Total precipitation and precipitation intensity >> runoff generation & transport of sediment and nutrients
+2 inches of total annual rainfall
Number of days of precipitation over 1 inch
Total amount of precipitation falling in the heaviest 1% of rainfall events
While temperature change cannot be controlled, the secondary impacts of increased rainfall and rainfall intensity can be mitigated through stormwater controls, offering an adaptation measure to provide resilience to anticipated climate change
Sources: 4th National Climate Assessment (2018); Northeast Climate Science Center at the University of Massachusetts Amherst (https://www.resilientma.org/)

## Slide 9: Green Stormwater Infrastructure
Target Pollutants – Nutrients & Sediment
Use Low-cost Controls Whenever Possible
Design for Low Maintenance
Adapt Designs to Maximize Pollutant Load Reduction
Phosphorus – Bioretention Soil Mix (No Compost!)
Nitrogen – Internal Storage Reservoir
Leaching Catch Basin, RIDOT Linear Stormwater Manual
Tree Well, Niantic River Watershed
Bioswale, New Haven, CT
Roadside Biofilter, Central MA

## Slide 10: Residential LID Practices
Disconnect driveways and roofs
Redirect stormwater to lawns, dry wells, rain barrels, or rain gardens
Maintain natural buffers
Reduce lawn size, water usage, and fertilizer

## Slide 11: Elements of the Project
Compile and Review Data
Characterize Watershed Pollutant Sources
Develop Green Infrastructure Retrofit Concepts – Design/Permit (1)
Residential and Watershed-Wide Practices
Municipal Bylaw Review and Recommendations
Public Involvement
and
Community Engagement
Resource Mapping
2010 Diagnostic Study
Monitoring data
Known/suspected sources
Summarize data
Field inventories
Conceptual designs for 5 sites
Size for future precipitation
Estimates of pollutant removal
Estimates of cost
Carry one (1) concept to permitting
Outreach materials
Low impact development
Lawn care
Non-structural source controls
Nitrogen Control
Wetlands
Stormwater
Zoning
Resilience Trail Signage
Mashpee TV – documentary and PSAs
Digital Media – Storymap and webpage
Meetings – listening session, walkshop

## Slide 12: Schedule
2021
Project Initiation
Data Review
2022
GI Retrofit Concepts
Design/Permitting
LID & Watershed Practices
M
J
J
F
M
A
S
O
N
D
Watershed Pollutant Source Characterization
Bylaw
Review
Outreach & Engagement

## Slide 13: Outcomes
Watershed Characterization Report
Five (5) Stormwater Green Infrastructure Retrofit Concepts
Design & Permitting for One (1) Retrofit Concept
Recommendations for Bylaws
Outreach Materials
  Resilience Trail Signage
  Storymap – Residential “makeover”
  Digital information
  Video (documentary & 3 PSAs)

## Slide 14: Questions & Discussion

## Slide 15: Santuit Pond Watershed
AECOM, 2010