## Slide 1
Mashpee Water Quality Monitoring Program
Summary of Nutrient Related Health of
Mashpee’s Estuaries (summer 2018)
Town of Mashpee
Mashpee Wampanoag Tribe
SMAST-UMASSD Collaboration
For Estuarine Restoration
Brian L. Howes, Director
Coastal Systems Program
School of Marine Science & Technology
University of Massachusetts – Dartmouth
July 22, 2019

## Slide 2: Major Anthropogenic Problem Facing Estuaries Globally
Habitat Degradation:
increased nitrogen loading is the major threat to estuaries, world-wide;
Nitrogen enrichment is causing impairments to estuarine resources in portions of most Cape Cod Estuaries.

## Slide 3: Status: Mashpee Waquoit Bay
Upper regions of each estuary showing the greatest level of nutrient related water quality decline. Eelgrass lost from both systems.

## Slide 4: Status: Mashpee Popponesset Bay
Upper regions of each estuary showing the greatest level of nutrient related water quality decline. Eelgrass lost from both systems.

## Slide 5: Nitrogen management is the only way to restore degraded estuarine habitat, primarily through:  Increased tidal exchange  Control of watershed nitrogen sources  Increased Nitrogen removal in transport
How do we restore and protect
our estuaries?

## Slide 6: Mashpee Water Quality Monitoring Program
Goals:
-- to assess the current nutrient related water quality of each estuary within the Town of Mashpee
-- to track short & long-term changes in embayment health
-- to yield site specific validation of the effectiveness of Nitrogen Management Alternatives and for TMDL compliance

## Slide 7: Estuarine Monitoring: Town of Mashpee
Waquoit Bay Water Quality Stations
2010-2018
18 estuarine stations monitored
4 sampling events

## Slide 8: Estuarine Monitoring: Town of Mashpee
Popponesset Bay Water Quality Stations
2010-2018
16 estuarine stations
4 sampling events

## Slide 9: Estuarine Monitoring 2018
N/P Ratio (molar)
Salinity (ppt)
P - Fertilizes
N - Fertilizes
Systems Need to be Managed for Nitrogen

## Slide 10: Estuarine Monitoring
Nitrogen Responsible for Phytoplankton Blooms

## Slide 11
Tidally Averaged Total Nitrogen (mg/L) Gradient
2010 N Loading
Build-out Loading

## Slide 12: Estuarine Monitoring Waquoit Bay Salinity
CR: Childs River, ER: Eel River, QR: Quashnet River, JP: Jehu Pond, HP: Hamblin Pond, WB: Waquoit Bay main basin

## Slide 13: Waquoit Bay Monitoring Results: Phytoplankton Biomass (Chlorophyll-a)
CR: Childs River, ER: Eel River, QR: Quashnet River, JP: Jehu Pond, HP: Hamblin Pond, WB: Waquoit Bay main basin
Sound
Highest in least flushed basins

## Slide 14
CR: Childs River, ER: Eel River, QR: Quashnet River, JP: Jehu Pond, HP: Hamblin Pond, WB: Waquoit Bay main basin
Stress
Water Quality Classification: SA
Waquoit Bay Monitoring Results: 20% Lowest D.O.
All Stations Showed Stress in 2018

## Slide 15: Waquoit Bay Monitoring Results: Total N
CR: Childs River, ER: Eel River, QR: Quashnet River, JP: Jehu Pond, HP: Hamblin Pond, WB: Waquoit Bay main basin
Threshold TN 0.5 mg/L
Threshold TN 0.38 mg/L
All Sites Over TMDL Nitrogen Threshold in All Years

## Slide 16: Waquoit Bay Shellfish Sites: Total N
Chart: Waquoit Bay TN: Long-Term vs 2010 - 2018
| JP-mid | GR-up | LR-GR | HP-mid | SeaR | WB-up | WB-lo
Long Term | 0.62467 | 0.60164 | 0.55379 | 0.52353 | 0.54988 | 0.48783 | 0.41565
2010-2012 | 0.72095 | 0.68321 | 0.62996 | 0.61513 | 0.60862 | 0.53486 | 0.44655
2013-2015 | 0.60987 | 0.61263 | 0.60342 | 0.63934 | 0.63182 | 0.53826 | 0.45748
2016 | 0.65171 | 0.6888 | 0.62469 | 0.65817 | 0.60864 | 0.57311 | 0.53878
2017 | 0.77463 | 0.57888 | 0.53134 | 0.56852 | 0.5301 | 0.51806 | 0.42412
2018 | 0.6221 | 0.66458 | 0.50817 | 0.5356 | 0.59354 | 0.6821 | 0.46782
WB: Waquoit Bay main basin, SeaR: Seapit River
Great+Little River = Hamblin Pond: Quahog Seeding = 10 Mill in 2014-2016, pre-2018 season 11 Mill seed
Seed
Seed
TN Lowered at Seeding Sites 2017-18

## Slide 17
Waquoit Bay Water Quality
2001-2018
Significant N enrichment in upper tributaries
Eastern embayments moderately N enriched
Quashnet continues to have poor water quality
2018 water quality, increased in terminal ponds (Hamblin, Jehu).
Estuarine Quality Index
Red = Poor
Yellow = Moderate
Blue = High
Long-term -
2016 only -
ER01
ER02
ER03
CR01
CR02
CR03
WB11
WB12
WB13
WB09
WB08
WB07
WB10
WB03
WB04
WB02
WB01
Estuarine Quality Index
Red = Poor
Yellow = Moderate
Blue = High
Long-term -
2018 only -

## Slide 18: Status: Mashpee Waquoit Bay
Upper regions of each estuary showing the greatest level of nutrient related water quality decline. Eelgrass lost from both systems.

## Slide 19
Nitrogen Levels: 2008
Nitrogen Levels: Build-Out

## Slide 20
MR: Mashpee River, SB: Shoestring Bay, Ock: Ockway Bay, Pinq: Pinquickset Cove, PCrk: Popponesset Creek, PB: Popponesset Bay
Monitoring Results: Popponesset Bay Salinity

## Slide 21: Popponesset Bay Monitoring Results: Phytoplankton Biomass (Chlorophyll-a)
MR: Mashpee River, SB: Shoestring Bay, Ock: Ockway Bay, Pinq: Pinquickset Cove, PCrk: Popponesset Creek, PB: Popponesset Bay
Nantucket Sound
Major Blooms in Each of Past 3 years

## Slide 22: Popponesset Bay 20% Lowest D.O.
MR: Mashpee River, SB: Shoestring Bay, Ock: Ockway Bay, Pinq: Pinquickset Cove, PCrk: Popponesset Creek, PB: Popponesset Bay
Water Quality Classification: SA
Stress
Oxygen Stress in ALL Tributary Basin over past 3 Summers

## Slide 23: Estuarine Monitoring Results: TN
MR: Mashpee River, SB: Shoestring Bay, Ock: Ockway Bay, Pinq: Pinquickset Cove, PCrk: Popponesset Creek, PB: Popponesset Bay
TN at ALL Stations Exceed TMDL TN Threshold

## Slide 24
Popponesset Bay Water Quality
Large and Significant N enrichment in upper tributaries; nutrient impairments throughout
Large phytoplankton blooms each summer
Slight TN decline associated with oyster culture in Mashpee River, but still impaired by N
Estuarine Quality Index
Red = Poor
Yellow = Moderate
Blue = High
Long-term -
2018 only -
PB05
PB06
PB07
SR5
PB04
PB03
PB02
PB08
PB11
PB10
PB09
PB12
PB13
PB14
PB15

## Slide 25: Status: Mashpee Popponesset Bay
Upper regions of each estuary showing the greatest level of nutrient related water quality decline. Eelgrass lost from both systems.

## Slide 26: Popponesset and Waquoit Bays
26
Findings:
Bays are showing little improvement in shellfish areas, are stable or declining in other areas. Almost all estuarine basins now showing impaired Habitat Quality.
The historically highest quality areas are now showing slow declines in habitat quality (e.g. Upper/Lower Main Basin of Popponesset Bay and Waquoit Bay)
Data indicate organic enrichment due to N inputs. Indicating that lowering N levels will reduce phytoplankton biomass and improve water clarity and oxygen conditions resulting in restored animal and plant habitats.
Results indicate that Monitoring Program is able to detect changes in response to implementation of management alternatives.

## Slide 27: Estuarine Monitoring: Popponesset Bay and Waquoit Bay
27
Findings:
Upper reaches of all estuarine basins are significantly impaired by excess nitrogen
Results indicate that Monitoring Program is able to detect changes in response to implementation of management alternatives.
Tracking water quality versus TMDL targets will be used to support adaptive management & reduce infrastructure costs as N removals start.

## Slide 28: Estuarine Monitoring: Popponesset Bay and Waquoit Bay
Mark Weissman Colin Grant, Bert Crothers, D. Sergio M Granville, Hurwitz, Jane & Rick Troubreidge, P. Zamrhitto, C Stringer
THANK YOU !

## Slide 29: “Knowledge and Need are the Basis of Innovation”
Questions & Discussion